## Slide 1: Welcome to

## Slide 2: How Cold is CodeMash?

## Slide 3: ArchitEcture overview
You Configure These
Pre-Existing Services
cm2017-ns Service Bus Namespace
ehdevices
Event Hub
SEND
ConnectTheDots Webhook
aka.ms/hcic
Web App
RCV
SEND

## Slide 4: Github repo
DOWNLOAD FILES FROM http://aka.ms/hcicsource

## Slide 5: Installing prerequisites
Installing prereqs, just a moment!

## Slide 6: Install node.js v6.9.4 Not v7.4.0
https://nodejs.org/

## Slide 7: Install prerequisites
Install Node v6.9.4 LTS (NOT v7.4.0) https://nodejs.org/ Need a version manager for node? Check out https://github.com/creationix/nvm for Mac OSx or Linux or http://github.com/coreybutler/nvm-windows for Windows
Download and install Python 2.x (not 3+) https://www.python.org/downloads/
On Windows? You *may* need Visual Studio C++ tools: http://aka.ms/msbuild2013
REBOOT AFTER

## Slide 8: Install the particle-cli
Windows: Open a command prompt
Mac: Open a terminal window (may need to use sudo)
npm install –g particle-cli

## Slide 9: Install the particle-cli
npm install particle-cli -g
If it doesn’t build right on Windows, try adding:
npm install particle-cli –g --msvs_version=2013

## Slide 10: DOWNLOAD THE SOURCE
DOWNLOAD FILES FROM http://aka.ms/hcicsource
On Windows, “unblock” the .zip before you extract it:
Right-click on .zip
Select Properties
Check “unblock”
Click “OK”

## Slide 11: Setting up and claiming the photon

## Slide 12: Assemble the photon and weather shield
Photon’s USB port on the same edge as the Rain and Wind sensor jacks

## Slide 13: Connect the photon to your computer via usb cable
On Windows? Install the driver: http://aka.ms/photondriver
Extract the .zip file to a folder on your computer:
Open Device Manager
Right click-on the un-recognized device
Select “Update Driver Software…”
Point to the folder where you extracted the driver
Complete the install
Note the COM port it is attached to

## Slide 14: Identify the attached photon
First find the COM port it is attached to: particle serial list
Then, get the device ID: particle serial identify
Copy the Photon ID to your clipboard and save somewhere for later

## Slide 15: Create a free particle.io account
Go to http://particle.io
Click on the “build” link: http://build.particle.io/build
Create an account using
  U: <id>@mailinator.com
  P: <id>

## Slide 16: Login to the particle-cli
From a command prompt / terminal window: particle login
Use the credentials for particle build account you created

## Slide 17: Claim and name your photon
Then, get the device ID, copy the reported ID to your clipboard (Make sure the Photon is in Listening Mode ): particle serial identify
Add the device to your account particle device add <id>
Name the device particle device rename <id> <newname>

## Slide 18: Configure the particle wifi
From the command prompt: particle serial wifi Follow the prompts to connect the WiFi: <your wifi ssid> <your wifi security mode> <your wifi cypher type> <your wifi password>

## Slide 19: Creating the webhook

## Slide 20: Download the webhook.json
aka.ms/hcicwebhook
Save it to a known folder on your computer
Open the webhook.json file to review it
YOU DO NOT NEED TO MAKE ANY CHANGES AT THIS POINT
Learn more about Particle Webhooks here: http://aka.ms/pwh

## Slide 21
{
"event": "HowColdIsCodemash",
"url": "https://cm2017-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "30fpGKkPgzpKYXrl5nxYbb6OwIN/2h2ulVHXCsWxrpU="
},
"mydevices": true
}

## Slide 22
{
"event": "HowColdIsCodemash",
"url": "https://cm2017-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "30fpGKkPgzpKYXrl5nxYbb6OwIN/2h2ulVHXCsWxrpU="
},
"mydevices": true
}
The name of the “event” that will invoke the webhook.
When you call Spark.publish(“HowColdIsCodemash", payload); from your Photon, the Particle cloud back end will trigger this webhook and publish your payload to the Azure Event Hub, specified by the “url”

## Slide 23
{
"event": "HowColdIsCodemash",
"url": "https://cm2017-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "30fpGKkPgzpKYXrl5nxYbb6OwIN/2h2ulVHXCsWxrpU="
},
"mydevices": true
}
The “url” of the Azure Event Hub that the data will be published to.
In this case, we are posting to the “cm2017-ns” service bus namespace into an event hub named “ehdevices”

## Slide 24
{
"event": "HowColdIsCodemash",
"url": "https://cm2017-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "30fpGKkPgzpKYXrl5nxYbb6OwIN/2h2ulVHXCsWxrpU="
},
"mydevices": true
}
The data will be sent to the url using an HTTP POST

## Slide 25
{
"event": "HowColdIsCodemash",
"url": "https://cm2017-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "30fpGKkPgzpKYXrl5nxYbb6OwIN/2h2ulVHXCsWxrpU="
},
"mydevices": true
}
The json template is used to create the data for the message that will be sent to the Azure Event Hub

## Slide 26
{
"event": "HowColdIsCodemash",
"url": "https://cm2017-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "30fpGKkPgzpKYXrl5nxYbb6OwIN/2h2ulVHXCsWxrpU="
},
"mydevices": true
}
{
“s”: ”Weather”,
“u”: “F”,
“m”: “Temperature”,
“v”: 79.234,
“o”: “My Organization”,
“d”: “My Device Name” “l”: “My Location”,
} Sample Payload from the Photon’s Particle.Publish() call

## Slide 27
{
"event": "HowColdIsCodemash",
"url": "https://cm2017-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "30fpGKkPgzpKYXrl5nxYbb6OwIN/2h2ulVHXCsWxrpU="
},
"mydevices": true
}
The values:
SPARK_PUBLISHED_AT and SPARK_CORE_ID
Are supplied by the Particle cloud back end

## Slide 28
{
"event": "HowColdIsCodemash",
"url": "https://cm2017-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "30fpGKkPgzpKYXrl5nxYbb6OwIN/2h2ulVHXCsWxrpU="
},
"mydevices": true
}
The Shared-Access-Signature key name, and key value used to access the Azure Event Hub
The key name and key used here are from an event hub that Michael Bolton has setup already in the cloud for you to use.

## Slide 29
{
"event": "HowColdIsCodemash",
"url": "https://cm2017-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "30fpGKkPgzpKYXrl5nxYbb6OwIN/2h2ulVHXCsWxrpU="
},
"mydevices": true
}
Restricts the webhook to being triggered only from events published from your own devices

## Slide 30: Create the particle webhook
From the command prompt, get in the same folder as the webhook.json file you downloaded, and run: particle webhook create webhook.json
Other particle-cli webhook commands include: particle webhook list particle webhook delete hookid

## Slide 31: Programming the photon

## Slide 32: Create the particleweathershield Sketch
Create a new “App” here: https://build.particle.io/build/new
Name it “ParticleWeatherShield”
Download the sketch from: aka.ms/hcicsketch
Copy the text from the downloaded ParticleWeatherShield.c file
Paste into the ParticleWeatherShield app in Particle Build

## Slide 33: Add the Weather Shield library
In the Particle Build web interface, click the “Libraries” icon
Search for the SparkFun_Photon_Weather_Shield_Library
Select it, and then click the “INCLUDE IN APP” button:
Then, select the “ParticleWeatherShield” app, and click the “ADD TO THIS APP” button

## Slide 34: Library include and fields
// This #include statement was automatically added by the Particle IDE.
#include "SparkFun_Photon_Weather_Shield_Library/SparkFun_Photon_Weather_Shield_Library.h"
Weather sensor;
char Org[] = “Initech";
char Disp[] = “Samirs Printer";
char Locn[] = “OH";

## Slide 35: Library include and fields
// This #include statement was automatically added by the Particle IDE.
#include "SparkFun_Photon_Weather_Shield_Library/SparkFun_Photon_Weather_Shield_Library.h"
char Org[] = "ORGANIZATION_NAME";
char Disp[] = "DISPLAY_NAME";
char Locn[] = "LOCATION";
//Create Instance of the Weather Shield
Weather sensor;
//The amount of time (in milliseconds) to wait between each publication of data
int sendDelay = 6000;

## Slide 36: Setup method
void setup()
{
//Open up the Serial port for local diagnostics
Serial.begin(9600);
//Initialize the I2C sensors and ping them
sensor.begin();

## Slide 37: Setup method
//The following two lines tell the sensor what mode to use
sensor.setModeBarometer();//Set to Barometer Mode
//These are additional MPL3115A2 functions the MUST be called for the sensor to work.
sensor.setOversampleRate(7);
//Give the sensors some time to initialize
delay(10000);
}

## Slide 38: Loop method, and sensor reading
void loop()
{
//Measure Relative Humidity from the HTU21D or Si7021
float h = sensor.getRH();
//Measure Temperature from the HTU21D or Si7021
float f = sensor.getTempF();

## Slide 39: Publish temperature data
// Generate the temperature data payload
char payload[255];
snprintf(payload, sizeof(payload), "{\"s\":\"Weather\", \"u\":\"F\", \"m\":\"Temperature\", \"v\": %f, \"o\":\"%s\", \"d\":\"%s\", \"l\":\"%s\"}", f,Org,Disp,Locn);
//Emit the payload to the serial port for monitoring purposes
Serial.println(payload);
// Send the temperature data payload
Particle.publish(“HowColdIsCodemash", payload);
//Wait for the specified "sendDelay" before sending the humidity data...
delay(sendDelay);
{
“s”: “Weather”,
“u”: “F”,
“m”: “Temperature”,
“v”: 79.234,
“o”: “ORGANIZATION_NAME”,
“d”: “DISPLAY_NAME” “l”: “LOCATION”,
}

## Slide 40: Groking the photon code
// Generate the humidity data payload
snprintf(payload, sizeof(payload), "{\"s\":\"Weather\", \"u\":\"%%\", \"m\":\"Humidity\", \"v\": %f, \"o\":\"%s\", \"d\":\"%s\", \"l\":\"%s\"}", h,Org,Disp,Locn);
// Emit the payload to the serial port for monitoring purposes
Serial.println(payload);
// Send the humidity data payload
Particle.publish(“HowColdIsCodemash", payload);
// wait for the specified "sendDelay" before looping...
delay(sendDelay); } // End of loop()
{
“s”: “Weather”,
“u”: “%”,
“m”: “Humidity”,
“v”: 25.345,
“o”: “ORGANIZATION_NAME”,
“d”: “DISPLAY_NAME” “l”: “LOCATION”,
}

## Slide 41: Modify the metadata properties
Put your own values in. Make sure that the “Display Name” is appropriate and identifies your Photon clearly: char Org[] = "ORGANIZATION_NAME"; char Disp[] = "DISPLAY_NAME"; char Locn[] = "LOCATION";

## Slide 42: Has anybody seen a red stapler?

## Slide 43: Save, verify and flash
Click the save icon to save your sketch:
Click the verify icon to compile and verify:
Click the flash icon to deploy your sketch:

## Slide 44: Monitoring your photon

## Slide 45: Monitoring photon via serial
particle serial monitor

## Slide 46: Monitoring webhook
Particle-cli: particle subscribe mine
Particle Dashboard: http://dashboard.particle.io/user/logs

## Slide 47: Monitor via the web
Click device names along the left to show or hide them in the graphs
http://aka.ms/hcic

## Slide 48: FIRE!!!!!!!!

## Slide 49: Jumping to Conclusions

## Slide 50: Where to go from here?
Publish other sensor values. There are TON’s of other sensors you can use. As an example, check out: http://aka.ms/sparkfunsensors
Don’t want to use our existing event hub & web site? Make your own event hub and publish to Power BI, or consume the data from a client app! Check out my step by step walkthrough at: http://aka.ms/ppws
Don’t want to be limited by the Particle Cloud’s rate limits? Try publishing to your own API: http://aka.ms/iotree

## Slide 51: resources:
This deck, and other event resources: http://aka.ms/whla
Info about Particle and Azure: https://www.particle.io/microsoft
Azure Documentation http://azure.microsoft.com
Azure Portal https://manage.windowsazure.com and https://portal.azure.com
Particle Documentation http://docs.particle.io

## Slide 52: IoT Logo

## Slide 53: arduino

## Slide 54: GALILEO BOARD

## Slide 55: LEDs

## Slide 56: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 57: cables

## Slide 60: Micro SD Cards
Font: Segoe UI Semibold